Nov. 12, 2012

EE214000 Electromagnetics, Fall

Quiz #6, Open books, notes (21 points)

- (3 points) What is the energy density stored in a thin parallel-plate capacitor with an electrode separation of d and a voltage of V across the two capacitor electrodes? Assume the permittivity of the dielectric between the electrodes is (.

Ans: The electric field across a thin parallel-plate capacitor is E = V/d. The energy density is.

2. (3 points) In “1”, the surface area of the electrode plate is S. Calculate the capacitance of the parallel-plate capacitor from the stored energy.

Ans: the total stored energy is

(

3. (5 points) In “1”, the top electrode is biased at V and the bottom electrode is grounded. What is the surface polarization charge density right below the top electrode?

Ans:

The surface polarization charge density is

4. (5 points) Calculate the capacitance per unit length of a coaxial transmission line with an inner conductor radius of Ri and outer conductor radius of Ro. Assume the   permittivity of the dielectric between the two conductors is (.

Ans: Assume a line charge density (l on the inner conductor. The electric field at r is  . The voltage across the two conductors is therefore .The capacitance per unit length is