## Slide 1: LAB 8: Program Design Pattern and Software Architecture
Chung-Ta King
National Tsing Hua University
CS 4101 Introduction to Embedded Systems

## Slide 2: Introduction
In this lab, we will learn
  To measure and evaluate the performance of embedded programs on MSP430 LaunchPad
  To design embedded programs using the state machine pattern

## Slide 3: Recall Software UART in Lab 6
Second half of main():
TimerA_UART_init(); // Start Timer_A UART
TimerA_UART_print("G2xx2 TimerA UART\r\n");
TimerA_UART_print("READY.\r\n");
for (;;) {
// Wait for incoming character
__bis_SR_register(LPM0_bits);
// Echo received character
TimerA_UART_tx(rxBuffer);
}
}
void TimerA_UART_print(char *string) {
while (*string) TimerA_UART_tx(*string++);
}

## Slide 4: TimerA_UART_tx()
void TimerA_UART_init(void) {
TACCTL0 = OUT; // Set TXD Idle as Mark = '1'
TACCTL1 = SCS + CM1 + CAP + CCIE;
// Sync, Neg Edge, Capture, Int
TACTL = TASSEL_2 + MC_2; // SMCLK, continuous mode
}
void TimerA_UART_tx(unsigned char byte) {
while (TACCTL0 & CCIE); // Ensure last char TX'd
TACCR0 = TAR; // Current state of TA counter
TACCR0 += UART_TBIT; // One bit time till first bit
TACCTL0 = OUTMOD0 + CCIE; // Set TXD on EQU0, Int
txData = byte; // Load global variable
txData |= 0x100; // Add mark stop bit to TXData
txData <<= 1; // Add space start bit
}

## Slide 5: UART TXD ISR
5
#pragma vector = TIMER0_A0_VECTOR __interrupt void Timer_A0_ISR(void) { static unsigned char txBitCnt = 10; TACCR0 += UART_TBIT; // Add Offset to CCRx if (txBitCnt == 0) { // All bits TXed? TACCTL0 &= ~CCIE; // All bits TXed, disable int txBitCnt = 10; // Re-load bit counter } else { if (txData & 0x01) { TACCTL0 &= ~OUTMOD2; // TX Mark '1’ } else { TACCTL0 ¦= OUTMOD2;} // TX Space '0‘ txData >>= 1; txBitCnt--; } }
Notes: 5
5

## Slide 6: Questions about the Code
Where does the program halt waiting for interrupts between transmission of bits?
How to know the duty cycle of TXD and RXD?
  A duty cycle is the time that MSP430 spends in active mode as a fraction of the duration of transmitting/receiving a bit in UART
  For 9600 baud, duration of a bit is 1/9600 sec.
  In full duplex, TXD and RXD may be intermixed. Thus, if duty cycle > 50%, bits may be missed!

## Slide 7: Duty Cycle of UART RXD
Signal on P1.2
Active mode
LPM3
CPU mode
ISR
Duty cycle =
Total time in ISRs
10 bits  cycle time

## Slide 8: Basic Lab 1 (1/2)
Modify your software UART program developed in Lab 6. Run the UART with 9600 baud, 8-bit data, and 1 stop bit. Measure the duty cycle in transmitting a data byte (1 start, 8 data, 1 stop bits). Transmit the calculated value of duty cycle back to PC to show on the screen. Then, do the same for receiving a byte.
Hint 1: Read TAR for the start and end time of ISR.
Hint 2: Do not transform an integer to a float in ISR.
Hint 3: The place where you put your code will affect the time you get.

## Slide 9: Basic Lab 1 (2/2)
To measure the receiving time on you LaunchPad, you should type a character at your PC terminal and let the LaunchPad calculate the duty cycle of receiving the typed character. Then LaunchPad transmits back the character and the measured values of the duty cycle. The values are printed.
EX: type “a” and you will see on your screen output: a RX: 40% TX: 38%

## Slide 10: Program Design Pattern

## Slide 11: Recall Software UART Again
The ISR handling RXD:
#pragma vector = TIMER0_A1_VECTOR
__interrupt void Timer_A1_ISR(void) {
static unsigned char rxBitCnt = 8;
static unsigned char rxData = 0;
switch (__even_in_range(TA0IV, TA0IV_TAIFG)) {
case TA0IV_TACCR1: // TACCR1 CCIFG - UART RX
TACCR1 += UART_TBIT; // Add Offset to CCRx
if (TACCTL1 & CAP) { // On start bit edge
TACCTL1 &= ~CAP; // Switch to compare mode
TACCR1 += UART_TBIT_DIV_2; // To middle of D0
} else { // Get next data bit
rxData >>= 1;

## Slide 12: ISR Handling RXD
12
if (TACCTL1 & SCCI) { // Get bit from latch rxData ¦= 0x80; } rxBitCnt--; if (rxBitCnt == 0) { // All bits RXed? rxBuffer = rxData; // Store in global rxBitCnt = 8; // Re-load bit counter TACCTL1 ¦= CAP; // Switch to capture __bic_SR_register_on_exit(LPM0_bits); // Clear LPM0 bits from 0(SR) } } break; } }
Wake up
main loop
Notes: 12
12

## Slide 13: ISR Actually Runs a State Machine
Start Bit
Data Bit
Stop Bit
Timer_up
/ Prepare RX data bits
Idle
Drop_edge
/Prepare RX stop bit
Timer_up && rxBitCnt > 0
/ Prepare RX next data bit
Timer_up && rxBitCnt = 0
/ Prepare RX stop bit
Timer_up / Return RX byte
Triggering events:
Falling edge
rxBitCnt == 0
Timer up

## Slide 14: Basic Lab 2 (1/2)
Measure temperature at 2 Hz using ADC10 from internal temperature sensor
  Up Mode: Flash red LED at 2 Hz. Whenever the temperature keeps rising for N consecutive samplings, flash red LED at 10 Hz.
  Down Mode: Same as Mode 1, except flashing green LED and change flashing rate when the temperature drops for N consecutive samplings. Hint : Define a variable ‘SAMPLING_CNT’ to keep the value N, and for the convenience of demo, set the value to 2.

## Slide 15: Basic Lab 2 (2/2)
The two modes are toggled whenever the button is pressed. System starts at Up Mode.
Draw a state machine describing this system, including states, triggering events, & actions.
  Hint: Timer-up may be considered as an event.
Implement the system using state machine.
  The switch-statement for the state machine may be implemented in main() or in individual ISR that corresponds to a triggering event.

## Slide 16: State Machine in main() (1/2)
void main(void) { while(1) { // go to low-power mode // disable interrupt switch(state) { case state1: // check event flags // perform corresponding actions // state = next_state // clear event flags case state2: ...} // enable interrupt } }

## Slide 17: State Machine in main() (2/2)
#pragma vector=XXXXX_VECTOR __interrupt void XXXXX_ISR(void) { // set event flags // wake up main() } #pragma vector=YYYYY_VECTOR __interrupt void YYYYY_ISR(void) { // set event flags // wake up main() }

## Slide 18: Bonus
Add a third mode: Up/Down Mode:
  Flash both LEDs at 2 Hz. Whenever the temperature keeps rising for N consecutive samplings, keep flashing red LED at 10 Hz. Whenever the temperature keeps dropping for N consecutive samplings, keep flashing green LED at 10 Hz. In all other cases, return to flash both LEDs at 2 Hz.

## Slide 19: LAB_8 DEMO RULE
2012/11/12
CS 4101 Introduction to Embedded Systems

## Slide 20: Basic_1
Type a character on terminal and print
"RX: N% TX: M%“
notice：the duty cycle must less then 50%
(duty cycle < 50%).
You have to explain how you calculate the duty cycle.
Random questions.

## Slide 21: Basic_2
Draw a state machine describing your system, including states, triggering events, & actions.
(Using 1 page PPT to draw the state machine.
2. We will check the flow of the program is the same as
the state machine
3. Random questions.
Notes: The switch-statement for the state machine may be implemented in main() or in individual ISR

## Slide 22: Precautions
You need to demo again if you can’t explain clearly.
Check the following requirement before demo your lab :
  1. Finish your lab and check it can run correctly.
2. Make sure you really understand what your
lab doing.